## Slide 1: Energy Band & Fermi level

## Slide 2: Fermi Energy
Maximum energy possessed by free electron
At absolute temperature
Zero Kelvin or -273.15 Celcius
It varies from material to material
Free electron conducts current

## Slide 3: Fermi Level
You can find 50% electrons here
At any temperature
Energy Band
Conduction Band
Valence Band
Fermi Energy Level = EF

## Slide 4: Intrinsic
Intrinsic semiconductor is pure.
Probability of finding an electron in CB is equal to probability of finding a hole in VB
PC (e) = Pv(h)
Energy Band
Conduction Band
Valence Band
Fermi Energy, Ef, in the middle in intrinsic

## Slide 5: N- type Extrinsic
Donor atom added
Number of electron is greater
Pc (e) > Pv (h)
Where is Fermi level? Comment.
Energy Band
Conduction Band
Valence Band
Fermi Energy Level = EF

## Slide 6: P- type Extrinsic
Acceptor atom added
Number of Holes is greater
Pc (e) < Pv (h)
Where is Fermi level? Comment.
Energy Band
Conduction Band
Valence Band
Fermi Energy Level = EF

## Slide 7: Rules
Electron Concentration=?
Electron Concentration at CB=?
Energy at CB =?
Energy at VB =?
Energy at Fermi level = Ef
Boltzman Constant =?
8.62x10^-5; Unit eV/K
Temperature =?

## Slide 8: Donor-Acceptor
When we add an atom that gives electron, it’s donor
Atom that takes electron is acceptor
So, nd = no
Question, does na have any relation with holes?
Yes. It is => na = Po
We know, electron concentration at conduction band of pure silicon
It is 2.8 X 10^ 19 electrons/ cm^3
We also know, electron concentration at valence band of pure silicon
It is 1.04 X 10^ 19 electrons/ cm^3

## Slide 9: Problem-Solution
A pure silicon is doped to n-type by adding donor electron of 2*10^19 /cm^3, T = 300k. Determine it’s Fermi level in terms of Conduction Band.
Apply rule 2.
Ec – Ef = KT ln (nc / no)
=( 8.62*10^-5 * 300 ) ln (2.8*10^ 19/2*10^ 19)
Ec – Ef = 0.0259 * ln (1.4) = 0.00868 eV
So, fermi level is below 0.00868 eV to conduction band

## Slide 10
Determine the position of the Fermi level w.r.t. the Valence band energy in p-type silcon at T=300k
na= 5*10^15 electrons/cm^3 and nd= 4*10^15 electrons/cm^3
Apply rule 4.
Ef – Ev = KT ln( nv/Po )
We know, nv = 1.04X10^19 electrons/cm^3
We also know, donor concentration is holes concentration, na = po = 5x10^15 electrons/cm^3
Ef – Ev = 0.025*7.64 eV = 0.191 eV
So, Ef = Ev + 0.191 eV
Fermi level is above valence band by …0.191 eV

## Slide 11
A silicon is doped so that it’s fermi level has gone close to 0.424 eV of C.B. Determine the doping level.
What type of semiconductor does it become after doping?
n-type.
Suppose, T = 300k
n0 =
Ec-Ef = 0.424 eV
Use law 1.
n0 = 2.17x10^12 electrons/cm^3

## Slide 13: Problem-Solution
Calculate the position of Fermi level in n-type silicon at T=300K w.r.t. the intrinsic Fermi level energy.
Given, Nd= 2x10^17 electrons/cm^3 and Na= 3X10^16 electrons/cm^3.